## Slide 1: Chapter 2 Basic Concepts, Faraday’s Law and CSTR Balances
Learning Objectives:
After this chapter, you should:
  Understand basic concepts of current, current density and voltage
  Distinguish between electrolytic and galvanic types of electrochemical cells and know the sign conventions used for electrodes in these cell types.
  Describe the differences between the galvanostatic and potentiostatic modes of cell operation and their advantages
  Know the sources of voltage loss in operating cells and how to determine the energy (or power) required/delivered by electrochemical cells
  Understand the derivation of Faraday’s Law and apply it to common situations in industrial processes such as multiple reactions at a single electrode
  Determine how potential and current are distributed in the two types of connection in multi-electrode cells
  Know how to use Faraday’s Law in CSTR balances in order to model continuous electrochemical processes

## Slide 2: Terminology and Definitions
Name | Symbol | SI Unit
Current |  | 
Current Density | or | 
Electric Potential |  | 
Electric Potential Difference |  | 
Electric Field |  | 
Power |  | 
Resistance |  | 
Conductance |  | 
Resistivity |  | 
Conductivity | (or ) | 
Molar Conductivity |  | 
Faraday Constant |  | 
Velocity |  | 
Mobility |  | or
Viscosity |  | 
Name | Symbol | SI Unit
Current |  | 
Current Density |  | 
Electric Potential |  | 
Electric Potential Difference |  | 
Electric Field |  | 
Power |  | 
Resistance |  | 
Conductance |  | 
Resistivity |  | 
Conductivity |  | 
Molar Conductivity |  | 
Faraday Constant |  | 
Velocity |  | 
Mobility |  | 
Viscosity |  | 
  The following table lists the various properties and their units to be used
  throughout this course.

## Slide 3: Basic Concepts: Current, Current Density and Voltage
Current (I):
Current gives the rate of charge transfer across a circuit or cell due to the combined flow of electrons and ions. It has the units of coulombs/sec or amperes (A). This is analogous to fluid flowrate through a pipe.
What is the total charge q (in coulombs) passed by a circuit over a period of time from t1 to t2?
Current density :
It is useful to normalize the total current with respect to the electrode area through which it flows. This is called the current density and has units of A m-2 , i.e.,
where A = electrode area normal to the flow of charge

## Slide 4: Basic Concepts: Current, Current Density and Voltage
Aanode = anode area normal to flow of current
Acathode = cathode area normal to flow of current
= current flowing through anode
= current flowing through cathode
Consider electrolytic cell containing single anode and single cathode.
total current = I ≠ +
total current = I = =
Anode and cathode are in series with each other
anode current density anode
We can define the current densities

## Slide 5: Basic Concepts: Current, Current Density and Voltage
Two Points to Remember !!
Although = , is not necessarily equal to since the
electrode areas can be different.
The figures on the previous 2 pages both show current I flowing in one direction through the electrode and connecting wires and electrons (e-) flowing in the other direction. It is important to realize that these do not represent different phenomena occurring in a wire or electrode; in fact, they are two different ways to represent the same thing.
Electrical current was first measured long before electrons were actually discovered and before electrons were found to be the actual charge carriers through wires, metals, electrical circuits, etc. Electrical current was arbitrarily taken to be the flow of positive charge through a circuit.
The flow of negative charge carriers (e-) in one direction is indistinguishable from the flow I of an equivalent amount of positive charge carriers in the opposite direction
  The current I in an electrochemical cell gives a measure of the flowrate of both types of charge carriers – electrons through the electrodes and connecting wires and ions through the electrolyte..

## Slide 6: Basic Concepts: Current, Current Density and Voltage
Consider the potential associated with charging two plates. This charging process is not spontaneous since systems prefer to be uncharged.
Let’s say we have two parallel plates separated by a gap. We then charge the plates to an equal and opposite sign.
Plate A is positively charged, i.e., it contains more positive charge carriers than negative carriers
Plate B is negatively charged.
Since each plate is charged, energy is required to maintain this state. This is the principle behind the energy storage device called a capacitor. Furthermore, additional energy must be put into the system if we want to charge the plates even more.
Voltage:
Voltage or electric potential difference is the difference in electric potential between two points and is defined as the work needed per unit of charge to move a test charge between the two points in a static electric field.
Everyone has a physical idea of how fluids move, what pressure drop means, etc. In the case of electricity, electrical potential seems much more abstract. Can we give a physical picture of what it means?
Voltage or potential drop across a cell is the driving force moving charge through the circuit.
This drop is analogous to pressure drop in fluid flow.

## Slide 7: Basic Concepts: Current, Current Density and Voltage
So if we want to further charge the plates by moving a positive charge q from plate B (negative) to plate A ( positive), this will require work WAB to be done on the system.
The voltage drop or potential drop between A and B is defined as the work WAB per charge q to move charge q from B to A , i.e.,
Due to the effect of Coulomb’s law and the preference for electroneutrality, this does not occur spontaneously. Electrical energy must therefore be supplied by the power source in order for the electrons to flow as shown in the diagram.
In an electrolytic cell, the terminals of the power supply are similar to the charged plates described above.
Electrons are continuously discharged from the negative terminal of the power supply and re-enter the power supply at the positive terminal during operation. In order for this to occur, electrons must jump across the “gap” from the positive side to the negative side of the power supply.

## Slide 8: Electrons as Reactants/Products
Water electrolysis in H2SO4
Pumps electrons
by inducing voltage difference
Electrons flow out of -ve terminal
+
Current flows in opposite direction (out of +ve terminal and into -ve terminal)
1
2
e
-
e
-
I
SO
4
2
-
, HSO
4
-
H
+
H
2
O → ½ O
2
+ 2H
+
+ 2e
-
2H
+
+ 2e
-
→H
2
I
power
supply
Electrolytic Cell
+
‒
Electrons flow back into +ve terminal

## Slide 9: Electrons as Reactants/Products
The “black boxes” of
electrochemical engineering
Must consider flow of electrons in and out of electrodes as they participate in electrode reactions in order to completely analyze electrochemical engineering problems
Reduction rxn (Cathodic rxn)
Oxidation rxn (Anodic rxn)
Anode
Cathode
1
2
e
-
e
-
I
SO
4
2
-
, HSO
4
-
H
+
H
2
O → ½ O
2
+ 2H
+
+ 2e
-
2H
+
+ 2e
-
→ H2
2
I
power
supply

## Slide 10: Electrochemical Cells as Electric Circuits
Current must flow through entire cell, not just electrical connections
  While no solid wires connect the electrodes in solution, charge is transported by ions dissolved in solvent (i.e., electrolyte)
Resistor
Capacitor
Inductor
Electrical circuit analogy:
Resistances due to:
Mass
transport
Reaction kinetics, etc.
Ionic current
Electrical current
Electrical current
Formation of the electrical double-layer
+
–
e
–
e
–
I
–
ve ions
+
ve ions
solution
load
–
+
e
–
I
e
–
I
I

## Slide 11: Constraint of Electroneutrality
Electroneutrality is condition whereby total positive charge matches total negative charge within a system, i.e., no net charge.
  Does not hold over small distances (e.g., over the double-layer) from the electrode/electrolyte interface
For every H+ consumed at electrode 2, another H+ must be transferred from bulk electrolyte to take its place at the electrode
and
a negative charge carrier (eg. SO42-, HSO4-)
must be transferred from the vicinity of electrode 2 back into bulk electrolyte.
In fact, both of these occur in order to preserve electroneutrality.
For every electron generated by the reaction at electrode 1, an electron is consumed by the reaction at electrode 2. Every electron generated at electrode 1 is transferred to electrode 2.
Implications:
1
2
e
-
e
-
I
SO
4
2
-
, HSO
4
-
H
+
H
2
O → ½ O
2
+ 2H
+
+ 2e
-
2H
+
+ 2e
-
→H
2
I
power
supply
Electrolysis of H2O

## Slide 12: Types of Electrochemical Cells
There are two basic types of electrochemical cells:
Electrolytic - Electrical energy is applied to drive electrochemical reactions that would not otherwise occur.
  Examples: chloro-alkali cell, electroplating
Galvanic – Spontaneous electrochemical reactions generate a flow of electrons and chemical products.
Examples: battery, corrosion, electroless plating

## Slide 13: Types of Electrodes and Electrode Reactions
Regardless of the type of an electrochemical cell, it must always
contain at least one cathode and one anode when current is flowing.
cathode - electrode at which a cathodic (reduction or consumption of electrons) reaction occurs
e.g., 2H+(aq) + 2e- → H2(g)
anode - electrode at which an anodic (oxidation or generation of electrons) reaction occurs
e.g., Fe2+(aq) → Fe3+(aq) + e-
These definitions apply for both electrolytic and galvanic cells.

## Slide 14: Sign Conventions in Electrochemical Cells
Sign conventions used in electrochemical cells can sometimes be confusing since you cannot always associate the cathode and anode with particular signs.
The sign of a cathode or anode depends upon type of cell, as shown below:
electrode electrolytic cell galvanic cell
cathode – +
anode + –
The reasons for these sign assignments are not arbitrary and will become
clearer later in the course.
What do “+” and “–” signs mean?
The (+) electrode has the more positive potential than the (–) electrode.

## Slide 15: Operating Modes of Electrochemical Cells
Galvanostatic mode:
Cell is operated at a controlled current. Voltage across cell cannot be simultaneously controlled, only measured.
Potentiostatic mode:
Cell is operated at a controlled cell voltage. Current through cell cannot be simultaneously controlled, only measured.
What is the advantage of galvanostatic mode?
The current (I) flowing through a circuit/cell and the voltage drop (E) across a circuit/cell are dependent on one another and so cannot be separately controlled. As a result, electrochemical cells are operated in one of two modes:
Process operates at known and controlled production rate. This is the first choice for most industrial operators unless problems warrant potentiostatic mode.
What is the advantage of potentiostatic mode?
When more than one reaction occurs simultaneously at an electrode (very common situation), application of appropriate applied cell voltage can enable one reaction to be favoured over another (i.e., higher selectivity)

## Slide 16: More Electrochemistry/Electrical Lingo…
Open-Circuit:
  In electrical field, an open-circuit is one where the electrical continuity in the circuit has been broken by an electrical interruption or gap in the path so that no current can flow.
  In electrochemistry, open-circuit denotes the more general condition in which no net current flows within a cell regardless whether or not an electrical interruption or gap in the circuit path exists.
Closed-Circuit:
  A closed-circuit is one that is complete, with good continuity for charge transfer throughout so that current can flow.
  Short-Circuit:
    Electrodes in cell are in direct physical contact. In an electrochemical cell, this usually creates an alternative pathway for current that does not include the electrolyte. As a result, no electrochemistry occurs in many short-circuit cells ; one notable exception of this is uniform corrosion where reactions are still able to occur.

## Slide 17: Voltage Losses in Operating Cell
– transport of ions in bulk electrolyte
– transport of electrons (i.e., conduction) through electrodes, connecting wires
– electrode reactions (involve ions and electrons)
– transport of ionic reactants and products across boundary layers close to electrode surfaces
– transport of charge carriers across membranes, junctions, etc.
As discussed previously, electrical potential is associated with work required to move charge in an electric field. The operation of an electrochemical cell involves a number of sub-processes that are associated with the movement of charge:
Each of these sub-processes consumes energy in order to occur; therefore, a price is paid to operate a cell and this takes the form of voltage (or energy) losses.
In an electrolytic cell, this raises the voltage (hence electrical energy) that must be supplied to drive electrode reactions at a given current (i.e., rate).
In a galvanic cell, this lowers the voltage at which current (hence electrical energy) can be delivered to an external load.
Much of what follows in this course is concerned with the sub-processes above and determining how they contribute to these voltage losses.

## Slide 18: Review of Reduction/Oxidation Reactions
Reduction reaction: a reactant gains electrons at the cathode:
  Net oxidation state of a reactant is lowered (i.e., reduced)
Oxidation reaction: a reactant loses electrons at the anode:
  Oxidation state of reactant is increased
H2O → ½ O2 + 2H+ + 2e-
O-2
O0
2H+ + 2e- → H2
H0
H+1
+1 → 0
- 2 → 0
Definition of oxidation state (OS):
Oxidation state is a number assigned to an atom in a compound, indicating the charge that the atom would have if all bonds were completely ionic.
Δ(OS)
Δ(OS)

## Slide 19: Distinction Between Oxidation and Reduction
Just remember:
  “An Ox and a Red Cat”
If you can’t remember what oxidation and reduction are:
  “LEO the lion goes GER”
Loss of
Electrons is
Oxidation
Gain of
Electrons is
Reduction

## Slide 20: Rules for Determining Oxidation States
Oxidation state of any free element (i.e., an element not bound to any other elements) is equal to zero
  e.g., Cu(s), H2(g), Cl2(g), S8(s) have an oxidation state of zero
Oxidation state of a monatomic ion is equal to the charge of the ion
  e.g., Na+(aq) has an OS of +1, Ca2+(aq) has an oxidation state of +2
Sum of oxidation states of all atoms in a species weighted according to their stoichiometric coefficients is equal to the overall charge of the species.
Sum of oxidation states of all atoms in a species weighted according to their stoichiometric coefficients is zero for a neutral species (i.e., a species without a charge).

## Slide 21: Additional Rules…
Alkali metals (Group 1 except H) always have OS of +1 or 0.
Alkaline earth metals (Group 2) always have OS of +2 or 0.
Fluorine (F) always has OS of -1 or 0.
Hydrogen usually has OS of +1 or 0.*
Oxygen usually has OS of -2 or 0.**
Halogens except fluorine (Group 17) usually have OS of -1 or 0.***
Group 16 elements usually have OS of -2 or 0, but can also have OS of +2,+4 or +6.
Group 15 elements usually have OS of -3 or 0, but can also have OS of +3 or +5
Some Exceptions:
* OS of hydrogen is -1 in hydrides
** OS of oxygen is -1 in peroxides, in superoxides and , +1 or +2 when bonded with F
*** OS of halogens can also be +1,+3,+4,+5,+7 when bonded to O or F

## Slide 22: Example: Determine the Oxidation States of the Atoms in the Following Species
FeO c) AlF4- e) AlOOH g) O2F
LiH d) OCl- f) PO43- h) NaO2
Notes: Many metals

## Slide 28: Michael Faraday (1791 – 1867)
One of the greatest experimentalists in physics and chemistry of all time
Discovered many important things:
  Electromagnetic induction (key principle behind electric motors, transformers, generators)
  Invented electromagnetic rotary devices and electric dynamo
  Diamagnetism
  Developed concept of fields in physics
  Discovered benzene
  Invented notion of oxidation states
  Electrolysis
  Faraday’s Laws
  1 unit (farad) and 1 constant (Faraday constant) named after him
He is considered to be the founder of electrochemistry

## Slide 29: Faraday’s 1st and 2nd Laws of Electrolysis
Faraday carried out metal deposition reactions in electrolytic cells from solutions containing metal salts. He measured the mass plated as a function of the charge passed and found:
  1st Law - mass produced is directly proportional to the total charge passed.
  2nd Law – ratio of the masses of any two metals formed with the same amount of charge depends only on the identity of the two metals; later when the concept of molecular weight was introduced, this ratio was found to be the ratio of their equivalent weights.
Recall: equivalent weight of ion Mn+ =
molecular weight of Mn+
charge of Mn+

## Slide 30: Faraday’s Law
Nowadays, Faraday’s Law can be derived straightforwardly from stoichiometry.
Faraday’s Law relates electronic charge transferred to mass reacted in an electron transfer reaction.
Consider the following general half-cell reaction occurring at an electrode:
where and are stoichiometric coefficients, and are ionic charges. In an operating cell, another half-cell reaction occurs at the other electrode.
number of electrons generated in producing moles of =
number of electrons generated per mole of produced =
total charge of the electrons generated per mole of produced =
total charge generated in producing moles of = =
electronic charge
𝓝av

## Slide 31
is a universal constant given the name Faraday constant F
∴
With this substitution, we end up with
Eqn (1) incorporates both Faraday’s 1st and 2nd laws.
If the process described in Eqn (1) occurs over a time period , we can write it in a rate form, i.e.,
As → 0 , this can be written in differential form, i.e.,
charge associated with an Avogadro’s number of electrons
(1)
cumulative form of Faraday’s Law

## Slide 32
How do we relate the rates of change of the different species participating in the reaction ?
reaction rate (mol s-1)
Substitution of this expression into the one on the bottom of the previous page yields
By definition, current I =
rate form of Faraday’s Law
“+” sign since and are on same side of reaction
“” sign since and are on opposite side of reaction
Relates production rates of and to current
∴ I =
(2)

## Slide 33
.
From Eqn (2), we see that I > 0.
As written above, the reaction is anodic when it proceeds from left to right.
If the above reaction proceeds from right to left, then > 0 and < 0.
If the reaction proceeds from left to right, then < 0 and > 0.
∴ I > 0 for anodic reaction
This is always valid
∴ I < 0 for cathodic reaction
This is always valid
I = +
(2)

## Slide 34
When discussing an operating cell, we usually only refer to the magnitude of the current that flows.
When considering the current to a single electrode, the sign of the current can be important.
Current density i at an electrode with area 𝒜 is:
i =

## Slide 35: Examples of Applying Faraday’s Law
Example 1:
Apply Faraday’s law to describe the current in terms of the production rates of H+ and H2 according to the following reaction:
  H2 → 2H+ + 2e-

## Slide 38: Examples of Applying Faraday’s Law
Example 2:
Apply Faraday’s law to describe the current in terms of the production rates of Pb and PbO2 in a lead-acid battery:
  Pb(s) + PbO2(s) + 2HSO4-(aq) + 2H+(aq) → 2PbSO4(s) + 2H2O(l)

## Slide 42: Applying Faraday’s Law to Batteries
The theoretical specific capacity of an electrode expressed in mAh/g is a useful performance metric for battery systems.
Graphite is the –ve electrode in today’s Li-ion batteries. Charging of this battery causes Li+ ions to load into the graphite structure. Fully charged graphite has stoichiometric composition LiC6. What is its theoretical specific capacity in mAh/g?
First question: To what quantity does 1 A h correspond?
Solution
⇒ charge
1 A h = 1 A (3600 s) = 3600 A s = 3600 C
The theoretical specific capacity in mA h/g represents maximum charge stored in an electrode per unit mass of the electrode.
This represents the maximum charge generated by an electrode on going from its fully charged state to its fully discharged state.
∴ 1 C = A h

## Slide 43
⇒ cumulative form – relates total charge transferred to yield a certain amount of product (Note: no rates are mentioned in question)
The complete discharge of the –ve graphite electrode can be written as follows:
C6Li → C6 + Li+ + e-
pure graphite
fully charged
fully discharged
Note: C6Li is not an actual compound per se. It reflects stoichiometry for the intercalation of Li into the graphite structure (i.e., 1 Li is associated with 6 C when graphite is fully charged).
43

## Slide 44
Now apply Faraday’s Law to the reaction above.
Charge generated can be related to the number of moles of pure graphite (i.e., C6) produced over its complete discharge by the following expression:
If is equal to the total number of moles of graphite in the electrode, then corresponds to the theoretical capacity of the electrode.
The stoichiometric coefficients for the reaction are:
With these coefficients, the expression above becomes:

## Slide 45
As shown earlier in this solution, 1 C = A h
If we normalize in terms of the mass of C6 in the electrode, we obtain the theoretical specific capacity, i.e.,
However, we recognize that
molecular weight of graphite
Use of this conversion in the previous relation above yields:

## Slide 46
When this is substituted into the expression above, we obtain:
theoretical specific capacity

## Slide 47: Current Efficiency
Usually, more than one electrode reaction occurs simultaneously on a single electrode. These reactions will occur as parallel, competitive processes.
Total current is split between all the reactions that occur on the electrode.
= total current through electrode
=
where = partial current due to
reaction j
This relation also applies to current densities
=
Important: Faraday’s Law can be applied to every electrode reaction
occurring on the electrode.

## Slide 48
Current efficiency for reaction j on an electrode is defined as:
Current efficiency is a quantity that applies to an electrode and not to the electrochemical cell as a whole.
The current efficiency can be determined for each reaction that occurs on the anode and then this procedure is repeated for the reactions that occur on the cathode.

## Slide 49: Current Efficiency Example
To illustrate the point that current efficiency is associated with each electrode and not to the cell as a whole, consider the following example:
The reactions occurring during zinc electrowinning are:
cathode: Zn2+ + 2 e- → Zn0(s) , current =
2 H+ + 2 e- → H2(g) , current =
anode: H2O(l) → ½ O2(g) + 2 H+(aq) + 2 e- , current =
What conditions hold?

## Slide 50
Furthermore, the current flowing through the electrodes is related to the current through the electrolyte as follows:
anode, electrolyte and cathode are connected in series with each other
∴ Ianode =
= Ielectrolyte
=
=
current flowing through electrolyte

## Slide 51
What is the current efficiency of Zn2+ reduction at the cathode?
What is the current efficiency of H+ reduction at the cathode?
What is the current efficiency of O2 evolution at the anode?
Only one reaction occurs at anode.
∴
Conclusion: Current efficiencies at cathode and anode are not necessarily equal to each other

## Slide 52: Energy Requirement/Generation
As discussed, the operation of an electrochemical cell involves either input of electrical energy (electrolytic cell) or generation of electrical energy (galvanic cell).
Not surprisingly, this energy is related to the two fundamental quantities associated with cell operation:
cell voltage Vcell – voltage drop across cell, as measured between +ve and –ve terminals of power supply or voltmeter
cell current Icell – magnitude of total current flowing through cell
If a cell operates at a total current Icell and cell voltage Vcell, then
electrical energy required (or generated) over time from 0 to t =
use current, not current density
(electrolytic cell)
Unit Check: 1 ampere - volt ≡ 1 A-V ≡ 1 J s-1 ≡ 1 W
power required
or
power generated
=
Vcell Icell
(units of W or J s-1)
(galvanic cell)
= Vcell Icell t
if Vcell and Icell are constant
(units of J)

## Slide 53: Electrical Connections in Multi-Electrode Cells
In practical situations, cells contain more than a single +ve electrode and –ve electrode.
This can be done via two different types of connection: i) monopolar and ii) bipolar
As will be shown, although the connections differ, both types of circuits still consist of the same basic building block:
→ a +ve electrode face / electrolyte/ –ve electrode face unit consisting of a +ve electrode separated from a –ve electrode by electrolyte
Note: This is identical to a cell with a single +ve electrode and –ve electrode.
Vj = voltage drop across each +ve / e /–ve unit
Ij = current flowing across each +ve / e /–ve unit
For convenience, this unit will be denoted as a +ve/ e /–ve unit in what follows.
How can the +ve and –ve electrodes be connected in such a cell ?

## Slide 54
The older and still commonly used method.
Every second electrode is suspended on a common conducting busbar connected to +ve terminal of power supply or voltmeter; these electrodes are +ve during operation.
Remaining electrodes are suspended on another busbar connected to –ve terminal of power supply or voltmeter; these electrodes are –ve during operation.
This creates an alternating sequence of +ve and –ve electrodes
All +ve electrodes are kept at one potential and all –ve electrodes at another potential. Total current is distributed between each +ve / e /–ve unit.
The +ve / e /–ve units are connected in parallel.
busbar
busbar
Plan view (i.e., each electrode is a flat sheet coming out of the plane of page)
Note: A busbar is a connection bar or strip that distributes current.
Monopolar cell:

## Slide 55
Vj = voltage drop across a +ve / e /–ve unit.
Ij = current flowing across a +ve / e /–ve unit.
N = number of +ve / e /–ve units in cell
Vcell = Vj
∴ power expended
or delivered
Note: In this case, a face is one side of an electrode sheet. Also, in this case. both sides of each electrode are involved in electrode reactions, except for the end electrodes. So, in the above example, N = 5.
Both sides of each electrode have the same polarity. This is the origin of the term “monopolar” connection.
Icell =

## Slide 56
Current Path in Monopolar Connection
Let’s look at the current path in a monopolar connection for an electrolytic cell more closely.
Current path:
1. flows from +ve terminal of power supply into +ve electrode,
2. splits into two equal paths that flow across electrolyte into –ve electrodes on either side,
3. flows out right ends of –ve electrodes where paths recombine and
4. recombined current flows into
–ve terminal of power supply
Overall, the current is split evenly between the two +ve / e /–ve units connected in parallel.
Current will flow wherever it can – as long as it can enter from power supply through +ve electrode across electrolyte and out through –ve electrode back to power supply.
Number of different pathways through which this can occur determines N (same as the number of +ve / e /–ve units in cell).
Each pathway is connected in parallel to each other and carries the same current of Icell / N.
As an example, consider cell with 1 +ve electrode and 2 –ve electrodes:

## Slide 57
Bipolar Cell:
Bipolar connection requires only external electrical connections to the two end electrodes.
Electrodes are not hooked up together by any wires or leads; they are only separated by electrolyte.
Current flows from +ve terminal in series from one electrode to the next until it reaches –ve terminal. The potential drops continuously on going from electrode to electrode from the +ve terminal end to the −ve terminal end.
The +ve / e /–ve units are connected in series.
Note: Vcell,mono above is equal to the cell voltage in the analogous monopolar cell shown on slide 54. Thus, the cell voltage of the bipolar cell is N times (N=5 in this example) larger than that of the monopolar cell.
No electrical connection to inner electrode leads!
VCELL,mono
Shown on the next page is the voltage distribution across a bipolar cell.

## Slide 58
A potential drop large enough to drive the process exists across the electrolyte from one electrode to the next.
A very small IR drop will exist through each electrode. Thus, one side of each electrode is at a slightly higher potential than the other.
One side of each electrode is the +ve electrode for one +ve / e /–ve unit; other side is the –ve electrode for the +ve / e /–ve unit on the other side.
Thus, one side of each electrode has +ve polarity and the other side has –ve polarity.
This is the origin of the term “bipolar”.

## Slide 59
For a bipolar connection,
Icell = Ij
electrodes in series with each other
includes IR drop through each electrode
∴ power expended
or generated
Vcell =
N = 5 in this example
Note: Ij, and N are defined exactly as they are in the monopolar case.
5 Vcell,mono

## Slide 60
Consider that the objective of the monopolar and bipolar circuits is to produce the same amount of chemical species at each electrode.
Then what occurs between the +ve electrode and –ve electrode faces in each basic unit above is the same regardless of the type of connection. Thus, Ij, and N in the expressions above are the same and so are the power requirement/generation for the two connections.
Which connection is more efficient – monopolar or bipolar?
As discussed, the two connections are built up from the same basic unit.
Where the monopolar and bipolar circuits differ is in how each of these basic units is connected to one another.
Surely, there must be some advantages to each type of connection. If not, why would we be worrying about the differences between them?

## Slide 61
Monopolar Versus Bipolar Connection
IMPORTANT: Monopolar cell operates at high current, low voltage.
Bipolar cell operates at low current, high voltage.
power is about the same
Advantages of bipolar connection
Fewer electrical connections in bipolar case.
2. Current path through the electrode in a monopolar connection is along the length of the electrode. Current path through a bipolar electrode is only through its thickness. This raises IR drop in monopolar cell compared to bipolar cell.
monopolar
(every electrode must be wired)
usually very small effect
bipolar
(only outer electrodes must be wired)
5 Vcell,mono
∴ set-up for bipolar circuit is simpler and leads to less IR drop for hardware

## Slide 62
Bipolar connection is preferred when cell is made up of a stack of many closely spaced electrodes, e.g. fuel cells, H2O electrolyzer. No separate wiring, busbars and connections of the individual electrodes is required.
Ohmic loss for the entire cell is equal to IcellRcell. Obviously, any cell should be designed so as to minimize this ohmic loss.
As stated previously, large-scale monopolar cells operate at high Icell , whereas large-scale bipolar cells operate at low Icell .
For large-scale operations, this can put unrealistic demands on electrical hardware for a monopolar cell since Icell will be very large and so the electrical resistance Rcell must be very low.

## Slide 63
In bipolar circuit, a small amount of current is lost near the ends of each electrode as bypass current that does not flow between each +ve / e /–ve unit and instead bypasses one and skips to the next. This increases the IR drop in electrolyte.
Much less bypass current occurs with monopolar connection.
Monopolar connection is preferred for metal finishing processes such as deposition, dissolution, electroplating and electromachining since the objective is normally to treat both sides of each electrode. If bipolar connection is used, only one side of each workpiece (i.e., electrode) is finished. If monopolar connection is used, both sides of each workpiece are finished.
Advantages of monopolar connection
bipolar
5 Vcell,mono

## Slide 64: Pb Plating Example
Electrolytic cell

## Slide 65: CSTR Model for Electrochemical Reactors
As with other chemical reactors, an electrochemical reactor can be modelled as a continuously stirred tank reactor (CSTR)
Main assumptions of CSTR model:
- perfectly mixed contents and uniform concentrations within reactor
∴ discharge concentrations are the same as concentrations within reactor
V
q
CM , CH
qf
CMf , CHf
Do molar balances on dissolved species over entire tank or reactor. Do not attempt balances on H2O (l), solid species or gas.
First consider reactor with monopolar connection.
Note: Only steady-state problems will be given in numerical examples during this course; transient problems may be given if the objective is to formulate, but not solve, mass balances.

## Slide 66
To illustrate how this works, consider the example of metal plating:
cathode: current =
Mn+(aq) + n e- → M0(s) (1)
anode: current =
H2O(l) → ½ O2(g) + 2 H+(aq) + 2 e- (2)
dissolved species: Mn+(aq), H+(aq)
Definition of symbols
Mn+ concentration in feed and discharge, respectively (mol m-3)
H+ concentration in feed and discharge, respectively (mol m-3)
volumetric flowrate of feed and discharge, respectively (m3 s-1)
solution volume within reactor (m3)
= total current at all cathodes in reactor (A)
= total current at all anodes in reactor (A)
Consider the case where
∴ solution volume remains constant
How to evaluate ?
– use Faraday’s Law for reaction (1)
– each term in Eqn (3) must have units of mol s-1 to be consistent with Faraday’s Law
Example 1
Transient balance on Mn+ ion:
rate of generation of Mn+ within reactor due to electrochemical reaction

## Slide 67
Application of Faraday’s Law to Mn+ in reaction (1) , i.e., Mn+(aq) + n e- → M0(s)
where number of moles of Mn+ in electrolyte
Remember that < 0; this also ensures < 0.
Thus, the balance for Mn+ becomes
(4)
IMPORTANT: and must account for reaction and current at all cathodes in reactor.
must use current, not current density, so that has units of mol s-1

## Slide 68
Transient balance on H+ ion:
How to evaluate ?
– use Faraday’s Law for reaction (2) H2O(l) → ½ O2(g) + 2 H+(aq) + 2 e-
Thus, the balance for H+ becomes
(6)
(7)
In addition to the balances, an expression relating the various currents is needed:

## Slide 69
How would the balances change if a bipolar cell were used?
and in Eqns (3) and (5) must account for rates of change in entire reactor
where N = number of cathodes on which M0(s) is plated
(or number of anodes on which H+ is generated)
Recall that in a bipolar cell is much lower than in order to carry out the same process.
where = current at each anode
(same as for bipolar cell)
rate of generation of Mn+ at each cathode =
rate of generation of H+ at each anode =
where = current at each cathode
(same as for bipolar cell)

## Slide 70
Example 2
What are the balance equations for the following scheme in a monopolar cell?
cathode: M1n1+(aq) + n1 e- → M10(s) , current =
M2n2+(aq) + n2 e- → M20(s) , current =
How are , and related?
= = +
=
M1n1+
M2n2+
H+:
dissolved species: M1n1+(aq), M2n2+(aq), H+(aq)
anode: H2O(l) → ½ O2(g) + 2 H+(aq) + 2 e- , current =
these are all total currents at all cathodes or anodes in reactor

## Slide 71
Example 3
As a final example, consider the following reactions in a monopolar cell.
cathode: Mn+(aq) + n e- → M0(s) , current =
2 H+(aq) + 2 e- → H2 (g) , current =
anode: H2O(l) → ½ O2(g) + 2 H+(aq) + 2 e- , current =
H+: H+ is consumed at the cathode, but also generated at the anode.
What is ?
anodic reaction: = 2 , = 2
cathodic reaction:
= 2 , = 2
Mn+
these are all total currents at all cathodes or anodes in reactor
dissolved species: Mn+(aq), H+(aq)

## Slide 72
∴
Thus, the balance for H+ is:
+
How are , and related?
= = + =
Question: Will the pH increase or decrease in the cell during this process ?
H+ is consumed at current at cathode
H+ is generated at current at anode
>
∴ > ⇒ pH decreases (solution becomes more acidic)

## Slide 73: Nickel Plating Example

## Slide 74
Assume the system is operating under steady-state conditions.